Design Document for a Sodium Ion Battery Charger

Introduction
This document outlines the design of a Graphical User Interface (GUI) that implements a Sodium Ion Battery (SIB) charger using a Tenma programmable power supply unit (PSU). The GUI is implemented in C++ and using the Qt package.
It should be noted that a separate thread is used to issue commands to the PSU. This implementation involves sending a command and waiting for a response. This will probably mean that some type of state machine will need to be employed.
User Interactions
Select Configuration File
Implemented as a file selection dialog.
No serial port can be selected until a valid configuration file has been selected.
Select Serial Port
Implemented as a drop down list of all the serial ports available on the device. The user selects the serial port to which is connected to the PSU.
Open
Implemented as a push button. The program will attempt to open the serial port selected by the user and communicate with an attached PSU.
No further action can be implemented until a PSU has been successfully opened.
Start
Implemented as a push button. Initially disabled and only enabled when a configuration file and a serial port connection has been successfully opened. It is disabled during a charge cycle.
Stop
Implemented as a push button. It is initially disabled and is only enabled during a charge cycle.
Pause
Implemented as a push button. It is initially disabled and is only enabled during a charge cycle.
Quit
Implemented as a push button. It is always enabled.
None Interactive Displays
PSU Details
The Identification details of the attached PSU are displayed.
Actual Voltage and Current Values
Chart
A chart will be displayed showing the actual voltages and currents during the entire charging cycle. The voltages will be displayed in units of millivolts using the left hand axis. The currents will be displayed in units of milliamps using the right hand axis. The lower axis will be a time axis and will use units of seconds.
Configuration File Details
The configuration file will be in the Microsoft “.ini” format and will be user selectable. Configuration files can be created by the user using a text editor of their choice.
The configuration file must contain the following parameters:
- MAX_CHARGE_PERIOD
  Maximum charging period in units of milliseconds. If the charging time period is exceeded then the charging cycle will be automatically terminated.
- UPDATE_PERIOD
  Charging cycle monitoring period in units of milliseconds. This is the time period over which checks on the PSU actual voltages and currents are obtained and the charging algorithm applied. It is also the the time period when the main window is updated with the actual values obtained.
- MAX_CONSTANT_CURRENT
  The maximum constant current in units of milliamps. This is the maximum current allowed when charging in the constant current mode.
- COMPLETED_CURRENT
  The completed current in units of milliamps. This is the current when charging in the constant voltage mode and is used to indicate when charging is complete.
- MAX_APPLIED_VOLTS
  The maximum applied voltage in units of millivolts. This is the maximum voltage that can be applied during the constant current, constant voltage or initialisation modes of charging.
- MIN_APPLIED_VOLTS
  The minimum applied voltage in units of millivolts. This is the minimum voltage that can be applied during the constant current, constant voltage or initialisation modes of charging.
- VOLTS_INCREMENT
  Voltage increments in units of millivolts. This is the voltage increment used when it is required to keep the charging current within the limits as determined by the maximum charge constant current and completed charge current parameters.
Charging Algorithm
The charging algorithm for this program is as outlined in the specification for the Hakadi 18650 1500mA battery and is described as having a constant current phase followed by a constant voltage phase.
It is assumed that the starting charging voltage has already been established using the initialisation algorithm.

The maximum allowed voltage applied to the battery is 4.1v.
The maximum charging current is 0.5C which in this case is 750mA (1500 / 2).
The charging is complete when the charging current reaches 0.05C. That is in this case 75mA (1500 / 20).
The specification shows that the battery is charged at constant current initially until the voltage required to maintain this current reaches a maximum value which in this case is 4.1v. That is that the output voltage is maintained at a level less than the maximum voltage such that the charging current does not exceed the 0.5C maximum.
Calling this constant current is perhaps a misnomer as it is expected that as the applied voltage approaches the maximum then the charging current will reduce and hence not be constant current.
The algorithm is fairly basic and is implemented as a loop with a user defined period as follows.
Initialisation Algorithm
The following algorithm is used to ensure that the battery and PSU do not incur any damage when the charging cycle starts.
Potential damage to the PSU may occur when a higher voltage is applied to the PSU terminals than the current PSU output voltage is programmed for.
Potential damage to the battery may occur if an excessive voltage and hence current is applied to it. Hence the algorithm starts with the maximum allowable charging voltage but with the PSU Over Current Protection enabled and set to the maximum allowable charging current.
The algorithm establishes a starting voltage for the charging algorithm.
The algorithm is fairly basic and is implemented as a loop as follows.
- The PSU output is disabled. It is assumed that the PSU output is always disabled whenever battery charging is NOT in progress.
- The PSU output voltage is initially set to the maximum allowed.
- The PSU output current is set to the maximum allowed.
- The PSU Over Current Protection PSU mode is set.
- The PSU output is enabled.
- The PSU status is checked to see if the output is disabled. That is that the Over Current Protection has disabled the PSU output.
- If the PSU output is disabled then the voltage to apply is decremented by the voltage increment.
- If the voltage has reached the allowed minimum then the initialisation has failed and is complete.
- If the PSU output has been disabled then the cycle is repeated but using the now decremented voltage as a starting point.
- The PSU output has not been disabled so the initialisation is complete and the currently applied PSU output voltage is the start voltage for the charging algorithm.